## Slide 1: CS 6332.001: Systems Security and Binary Code Analysis Lecture 10
Kangkook Jee
Oct 30, 2025

## Slide 2: Outline
Virtualization principles
Binary translator
Case study: Light-weighted virtualization; container, docker

## Slide 3: Virtualization

## Slide 4: Virtualization Intro
Virtualization Overview
  Taxonomy
  CPU virtualization, memory space virtualization, device virtualization
Binary Translators
Light-weighted Virtualization (Containers)
Beginning of many innovations we see today
  Cloud, big data, ML and many more

## Slide 5: What is Virtualization?
A virtual machine monitor (VMM a.k.a. hypervisor) is a “kernel” where OSes are ‘applications’
  Abstract memory (guest physical addresses to machine physical)
  Multiplex between OSes and trap on specified exceptions/ violations
  Provide a consistent & abstracted view of hardware
Well-designed architecture (mostly) cleans a lot of crufts needed for legacy support
  Originally no support for real-mode
  64-bit aware, no PAE needed
  Allows VMM to be very small code base

## Slide 6: Isomorphism
Formally, virtualization involves the construction of an isomorphism from guest state to host state
Notes: * Virtualization software constructs an isomorphism from guest to host.
* All guest state S is mapped onto host state S’ through some function V(S).
* Additionally for every state changing operation e(S) in the guest there is a corresponding state changing operation e’(S’) in the host.
* Virtualization software must implement V() and e().
[KJEE]: Examples?
[TODO]: We can improve figure

## Slide 7: Types of Virtualization
Process Virtualization
  Language construction
    Java, .NET
  Cross-ISA emulation
    Running Android emulator
  Application virtualization
    Sandboxing
Device Virtualization
  RAID, NAT, Bridging
System Virtualization
  Type-1: VMWare, Xen
  Type-2: VirtualBox, VMWare Workstation, Fusion Microsoft Hyper-V
Light-Weighted Virtualization (Container)
  Container

## Slide 8: Taxonomy
Process VMs
System VMs
Same
ISA
Different
ISA
Same
ISA
Different
ISA
Dynamic
Translators
Hardware
VMs
Whole-System
Emulators
Dynamic Binary
Optimizers
HLL VMs
Type-2, Type-3
VMs
Co-designed
VMs
qemu-process,
JVM, Python VM
Notes: [KJEE] What is Multi-programmed systems? --- https://en.wikipedia.org/wiki/THE_multiprogramming_system
HLL - https://cs.nyu.edu/courses/spring14/CSCI-GA.3033-015/lecture6.pdf
Co-designed VMM: A codesigned VM has no native ISA applications. Instead, the VMM appears to be part of the hard- ware implementation
From “The Architecture of Virtual Machines “

## Slide 9: Software vs. Hardware Virtualization
ASPLOS 2006

## Slide 10: Virtualization Properties: Isolation
Fault Isolation
  Fundamental property of virtualization
Software Isolation
  Software Versioning
  DLL hell
Performance Isolation
  Accomplished through scheduling and resource allocation
Notes: First, virtualization provides isolation. Isolation is key for many applications and comes in several flavors.
Fault Isolation. If one virtual machine contains a buggy operating system, that OS can start scribbling all over physical memory. These wild rights must be contained within the VM boundaries.
Performance Isolation. Ideally VMs performance would be independent of the activity going‐on on the hardware. This must be accomplished by smart scheduling and resource allocation policies in the monitor.
Software Isolation. Most of the issues with computers today are complex software configurations. DLL hell on PCs, operating system and library versions, viruses, and other security threats. VMs are naturally isolated for each other by running in separate software environments.

## Slide 11: Virtualization Properties: Encapsulation
All VM state can be captured into a file
  Operate on VM by operating on file
  mv, cp, rm
Portability
  Independent of physical hardware
  Enables migration of live, running VMs
Complexity
  Proportional to virtual HW model
  Independent of guest software configuration
Notes: Encapsulation is the property that all VM state can be described and recorded simply. The VM state is basically the dynamic memory, static memory, and the register state of the CPU and devices. These items typically have a simple layout and are easy to describe. We can checkpoint a VM by writing out these items to a few files. The VM can be moved and copied by moving these files around. You can think about this as similar to doing a backup at the block level vs. doing a backup by recording all the packages, configuration and data files that encompass a file system.

## Slide 12: Virtualization Properties: Interposition
All guest actions go through hypervisor (monitor)
Monitor can inspect, modify, deny operations via Instrumentation
Ex)
  Compression
  Encryption
  Profiling
  Translation
  Reference Monitor
12
Subject
Object
Op request
Op response
Reference Monitor
CFG
Policy
Notes: At some level all access to the hardware passes through the monitor first. This gives the monitor and chance to operate on these accesses. The best example of this is encrypting all data written to a disk. The advantage of this is that it does it without the knowledge of the OS.

## Slide 13: Virtualization vs. Emulation
Emulation?
  QEMU runs ARM code from Intel machine
  Need to handle all instructions
Virtualization
  Run Windows from Linux
  Need to handle sensitive + privileged instructions
    Rest instructions can run natively
  Privileged instructions: make changes to CPU status
  Sensitive instructions: make changes to global system status
  Regular (benign) instructions: the rest

## Slide 14: Special Instructions
Privileged instructions
  The set of instructions that your ISA defines as privileged
  Only can be executed in “Ring-0” (e.g., Kernel Mode)
  E.g., I/O instruction, halt, Context switching
Sensitive instructions
  observes or modifies privileged machine state that can be used to change the current processor’s privilege level
  E.g., most instructions that we have dealt with
User-sensitive instruction
  Sensitive instruction that executes in user/unprivileged mode
Notes: https://www.geeksforgeeks.org/privileged-and-non-privileged-instructions-in-operating-system/
https://patents.google.com/patent/US6704925

## Slide 15: Sensitive but Non-privileged Instruction
cpuid: CPU identification
rdtsc: Read Time-Stamp Counter
Notes: https://c9x.me/x86/html/file_module_x86_id_45.html
https://www.felixcloutier.com/x86/rdtsc

## Slide 16: Sensitive but Non-privileged Instruction
cli: Clear Interrupt Table
sti: Set Interrupt Table
popf: restore EFLAGS register
Updates to `CR3` register
  Special register for virtual memory management
  Holds physical address

## Slide 17: Strictly Virtualizable
Privileged instructions (vs. User instructions)
  Only executed inside Kernel (ring-0)
  E.g., INVLPG, HLT …
Sensitive (System) Instructions (vs. innocuous/user instructions )
  Influences global system stage
  CLI, STI …
Goldberg’s Theorem 1
  For any conventional third-generation computer, a virtual machine monitor may be constructed if the set of sensitive instructions for that computer is a subset of the set of privileged instructions.
an efficient
Satisfies condition – efficiently virtualizable
Does not satisfy condition

## Slide 18: Trap and Emulate
Guest OS + Applications
Hypervisor (Virtual Machine Monitor)
Page
Fault
Undef
Instr
vIRQ
MMU
Emulation
CPU
Emulation
I/O
Emulation
Unprivileged
Privileged
A trap, also known as an exception or a fault, is typically a type of synchronous interrupt caused by an exceptional condition (e.g., breakpoint, division by zero, invalid memory access).
Expensive!
How can we trap sensitive but non-privileged instructions?
Notes: Direct execution
vIRQ?
a trap, also known as an exception or a fault, is typically[NB 1][1] a type of synchronous interrupt caused by an exceptional condition (e.g., breakpoint, division by zero, invalid memory access).

## Slide 19: System Virtualization Implementations
Notes: https://www.techtarget.com/searchitoperations/definition/AMD-V-AMD-virtualization

## Slide 20: Hardware Assisted Virtualization
Intel VT-X, AMD-V
  Modern CPUs support virtualization extensions
To reduce Trap and Emulate overheads
  Software (kernel)  Hardware
Under VT-X CPU operates on
root and non-root modes
Orthogonal to
  Privilege rings (0-3)
  real, protected, long modes etc.

## Slide 21: Binary Translator Workflow
Translator
Guest
Code
Translation
Cache
Callouts
TC
Index
CPU Emulation
Routines
TC: Translation Cache

## Slide 22: Basic Blocks
vPC
mov ebx, eax
cli
and ebx, ~0xfff
mov ebx, cr3
sti
ret
Guest Code
Straight-line code
Control flow
Basic Block
cli: clear interrupt, sti: set interrupt
cr3: control register

## Slide 23: Basic Blocks
vPC
mov ebx, eax
cli
and ebx, ~0xfff
mov ebx, cr3
sti
ret
Guest Code
Straight-line code
Control flow
Basic Block
cli: clear interrupt, sti: set interrupt
cr3: control register

## Slide 24: Binary Translation
vPC
mov ebx, eax
cli
and ebx, ~0xfff
mov ebx, cr3
sti
ret
mov ebx, eax
call HANDLE_CLI
and ebx, ~0xfff
mov [CO_ARG], ebx
call HANDLE_CR3
call HANDLE_STI
jmp HANDLE_RET
start
Guest Code
Translation Cache
Notes: Dynamic binary translation is used in virtualizing the CPU by translating potentially dangerous (or non-virtualizable) instruction sequences one-by-one into safe instruction sequences.
It works like this:
The monitor inspects the next sequence of instructions. An instruction sequence is typically defined as the next basic block, that is all instructions up to the next control transfer instruction such as a branch. There may be reasons to end a sequence earlier or go past a branch but for now let’s assume we go to the next branch.
Each instruction is translated, and the translation is copied into a translation cache.
Instructions are translated as follows:
  Instructions which pose no problems can be copied into the translation cache with modification. We call these “ident” translations.
  Some simple dangerous instructions can be translated into a short sequence emulation code. This code is placed directly into the translation cache. We call this “inline” translation. An example is the modification of the Interrupt Enable flag (CLI).
  Other dangerous instructions need be performed by emulation code in the monitor. For these instructions calls to the monitor are made. These are called “Call-outs”. An example of these is a change to the page table base (CR3).
  The branch ending the basic block needs a call out.
The monitor can now jump to the start of the translated basic block with the virtual registers in the hardware registers.
So dangerous instructions can be privileged instructions, non-virtualizable instructions, control flow, memory accesses.
CR3[edit]
Typical use of CR3 in address translation with 4 KiB pages
Used when virtual addressing is enabled, hence when the PG bit is set in CR0. CR3 enables the processor to translate linear addresses into physical addresses by locating the page directory and page tables for the current task. Typically, the upper 20 bits of CR3 become the page directory base register (PDBR), which stores the physical address of the first page directory entry. If the PCIDE bit in CR4 is set, the lowest 12 bits are used for the process-context identifier (PCID).[1]

## Slide 25: Binary Translation
vPC
mov ebx, eax
cli
and ebx, ~0xfff
mov ebx, cr3
sti
ret
mov ebx, eax
mov [CPU_IE], 0
and ebx, ~0xfff
mov [CO_ARG], ebx
call HANDLE_CR3
mov [CPU_IE], 1
test [CPU_IRQ], 1
jne
call HANDLE_INTS
jmp HANDLE_RET
start
Guest Code
Translation Cache
Notes: Dynamic binary translation is used in virtualizing the CPU by translating potentially dangerous (or non-virtualizable) instruction sequences one-by-one into safe instruction sequences.
It works like this:
The monitor inspects the next sequence of instructions. An instruction sequence is typically defined as the next basic block, that is all instructions up to the next control transfer instruction such as a branch. There may be reasons to end a sequence earlier or go past a branch but for now let’s assume we go to the next branch.
Each instruction is translated, and the translation is copied into a translation cache.
Instructions are translated as follows:
  Instructions which pose no problems can be copied into the translation cache with modification. We call these “ident” translations.
  Some simple dangerous instructions can be translated into a short sequence emulation code. This code is placed directly into the translation cache. We call this “inline” translation. An example is the modification of the Interrupt Enable flag (CLI).
  Other dangerous instructions need be performed by emulation code in the monitor. For these instructions calls to the monitor are made. These are called “Call-outs”. An example of these is a change to the page table base (CR3).
  The branch ending the basic block needs a call out.
The monitor can now jump to the start of the translated basic block with the virtual registers in the hardware registers.
So dangerous instructions can be privileged instructions, non-virtualizable instructions, control flow, memory accesses.
CR3[edit]
Typical use of CR3 in address translation with 4 KiB pages
Used when virtual addressing is enabled, hence when the PG bit is set in CR0. CR3 enables the processor to translate linear addresses into physical addresses by locating the page directory and page tables for the current task. Typically, the upper 20 bits of CR3 become the page directory base register (PDBR), which stores the physical address of the first page directory entry. If the PCIDE bit in CR4 is set, the lowest 12 bits are used for the process-context identifier (PCID).[1]

## Slide 26: Basic Binary Translator

## Slide 27: Basic Binary Translator – Part 2

## Slide 28: Controlling Control Flow
vEPC
test eax, 1
jeq
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
test eax, 1
jeq
call END_BB
call END_BB
start
Guest Code
Translation Cache
ret

## Slide 29: Controlling Control Flow
vEPC
test eax, 1
jeq
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
test eax, 1
jeq
call END_BB
call END_BB
Guest Code
Translation Cache
ret
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
call HANDLE_RET
eax == 0
find
next

## Slide 30: Controlling Control Flow
vEPC
test eax, 1
jeq
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
test eax, 1
jeq
jmp
call END_BB
Guest Code
Translation Cache
ret
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
call HANDLE_RET
eax == 0

## Slide 31: Controlling Control Flow
vEPC
test eax, 1
jeq
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
test eax, 1
jeq
jmp
call END_BB
Guest Code
Translation Cache
ret
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
call HANDLE_RET
eax == 1
find
next
mov [ecx], eax
call HANDLE_RET

## Slide 32: Controlling Control Flow
vEPC
test eax, 1
jeq
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
test eax, 1
jeq
jmp
jmp
Guest Code
Translation Cache
ret
add ebx, 18
mov ecx, [ebx]
mov [ecx], eax
call HANDLE_RET
eax == 1
mov [ecx], eax
call HANDLE_RET

## Slide 33: Issues with Binary Translation
Translation cache index data structure
PC Synchronization on interrupts
Self-modifying code
  Notified on writes to translated guest code

## Slide 34: Other Users for Binary Translation
Cross ISA translators
  Digital FX!32
Optimizing translators
  Pintool, DynamoRIO, Valgrind
High level language byte code translator
  Java Virtual Machine
  .NET / CLI
Notes: FX!32 is a software emulator program that allows Win32 programs built for the Intel x86 instruction set to execute on DEC Alpha-based systems running Windows NT.
FX!32 achieved speeds for Win32 x86 applications that ran 40-50% as fast as native x86 code

## Slide 35: Case Study: Binary-Only Program Instrumentation (without Source Code)
Dynamic Binary Instrumentation
  Useful tool for program instrumentation and investigation for DYNAMIC analysis
Intel PIN
  Most popular, developed and supported by Intel
  Supports IA32, x86_64 for Linux and Windows
DynamoRIO
  Similar architecture with Intel PIN
  Lower-level API with finer control
    E.g., Manual register spill / fill
  Support for ARM
Valgrind
  Heavy-weighted instrumentation
  Wide architecture coverage VEX IR
  MEMCHECK runs on Valgrind
Notes: [TODO] Add more contents later

## Slide 36: Process Virtualization
process
operating system
process
process
process
thread
thread
thread
thread
thread
thread
thread
thread
thread
thread
A
B
C
D
E
F
A
B
C
D
E
F
thread
thread

## Slide 37: Design Goals
Efficient
  Aiming for near-native performance (?)
Transparent
  Match native behavior
Comprehensive
  Control every instruction, in any application
Customizable
  Adapt to satisfy disparate tool needs

## Slide 38: DynamoRIO History
Google sponsors Dr. Memory
2001
VMware
acquires Determina
Determina
security startup
open-sourced BSD license
binary releases
DynamoRIO
@MIT
2003
2007
2010
2002
2009
Derek Bruening @Google
Notes: Dr. Memory
LLVM + ASAN

## Slide 39: Direct Code Modification
Kernel32!TerminateProcess:
7d4d1028 7c 05 jl 7d4d102f
7d4d102a 33 c0 xor %eax,%eax
7d4d102c 40 inc %eax
7d4d102d eb 08 jmp 7d4d1037
7d4d102f 50 push %eax
7d4d1030 e8 ed 7c 00 00 call 7d4d8d22
e9 37 6f 48 92 jmp <callout>

## Slide 40: Debugger Trap Too Expensive
Kernel32!TerminateProcess:
7d4d1028 7c 05 jl 7d4d102f
7d4d102a 33 c0 xor %eax,%eax
7d4d102c 40 inc %eax
7d4d102d eb 08 jmp 7d4d1037
7d4d102f 50 push %eax
7d4d1030 e8 ed 7c 00 00 call 7d4d8d22
cc int3 (breakpoint)

## Slide 41: Basic Interpreter
interpreter
fetch
decode
execute
application code
bar()
foo()
A
B
C
D
E
F
Slowdown: 300x

## Slide 42: Improvement #1: Basic Block Cache
application code
bar()
foo()
A
B
C
D
E
F
DynamoRIO
basic block cache
A
C
D
E
F
Slowdown: 300x
25x

## Slide 43: Example Basic Block Fragment
add %eax, %ecx
cmp $4, %eax
jle $0x40106f
add %eax, %ecx
cmp $4, %eax
jle <stub0>
jmp <stub1>
mov %eax, eax-slot
mov &dstub0, %eax
jmp context_switch
mov %eax, eax-slot
mov &dstub1, %eax
jmp context_switch
frag7:
stub0:
stub1:
dstub0
target: 0x40106f
dstub1
target: fall-thru

## Slide 44: Direct Linking
add %eax, %ecx
cmp $4, %eax
jle $0x40106f
add %eax, %ecx
cmp $4, %eax
jle <frag8>
jmp <stub1>
mov %eax, eax-slot
mov &dstub0, %eax
jmp context_switch
mov %eax, eax-slot
mov &dstub1, %eax
jmp context_switch
frag7:
stub0:
stub1:
dstub0
target: 0x40106f
dstub1
target: fall-thru

## Slide 45: Improvement #2: Linking Direct Branches
application code
bar()
foo()
A
B
C
D
E
F
DynamoRIO
basic block cache
A
C
D
E
F
Slowdown: 300x 25x
3x

## Slide 46: Improvement #3: Linking Indirect Branches
application code
bar()
foo()
A
B
C
D
E
F
DynamoRIO
basic block cache
A
C
D
E
F
Slowdown: 300x 25x 3x
indirect branch lookup
1.2x

## Slide 47: Indirect Branch Transformation
ret
mov %ecx, ecx-slot
pop %ecx
jmp <ib_lookup>
frag8:
...
...
...
ib_lookup:

## Slide 48: Improvement #4: Trace Building
Traces reduce branching, improve layout and locality, and facilitate optimizations across blocks
  We avoid indirect branch lookup
Next Executing Tail (NET) trace building scheme [Duesterwald 2000]
I
A
B
D
G
E
C
F
H
J
K
L
A
B
E
F
H
D
G
K
J
basic block cache
trace cache

## Slide 49: Incremental NET Trace Building
J
K
G
G
J
K
G
K
J
K
G
K
J
G
G
basic block cache
trace cache

## Slide 50: Improvement #4: Trace Building
application code
bar()
foo()
A
B
C
D
E
F
DynamoRIO
basic block cache
A
C
D
E
F
trace cache
A
C
D
E
F
?
Slowdown: 300x 25x 3x 1.2x
indirect branch lookup
ind. br. stays on trace?
1.1x

## Slide 51: Base Performance
SPEC CPU2000
Desktop
Server

## Slide 52: Base Performance: SPEC 2006

## Slide 53: ARM: Preliminary Performance Comparison
Chart: Normalized Execution Time
| 401.bzip2 | 403.gcc | 429.mcf | 445.gobmk | 456.hmmer | 458.sjeng | 462.libquantum | 464.h264ref | 473.astar | 433.milc | 444.namd | 447.dealll | 453.povray | 470.lbm | har_mean
AArch32 No Trace | 1.17 | 1.9 | 1.07 | 2.02 | 1.61 | 2.12 | 1.09 | 2.41 | 1.5279
AArch64 No Trace | 1.18 | 2.02 | 1.02 | 2.41 | 1.59 | 2.3 | 1.12 | 2.26 | 1.22 | 1.12 | 1.08 | 2.01 | 2.11 | 1.05 | 1.4434
x86-64 With Trace | 1.1 | 1.5 | 0.98 | 1.52 | 1.4 | 1.48 | 1.02 | 1.37 | 1.05 | 1.005 | 1.01 | 1.3 | 1.35 | 0.98 | 1.1842
AArch64 With Trace | 1.13 | 1.71 | 0.98 | 2.25 | 1.51 | 1.72 | 1.03 | 1.39 | 1.07 | 1.01 | 1.15 | 1.65 | 1.42 | 1.02 | 1.2781

## Slide 54: Sources of Overhead
Extra instructions
  Indirect branch target comparisons
  Indirect branch hash-table lookups
Extra data cache pressure
  Indirect branch hash-table
Branch mis-predictions
  Calls and returns turn into jumps on some architectures
Application code modification